## Slide 1: Instructor’s Electronic Curriculum Resource- For Techniques in Noninvasive Vascular Diagnosis-4th edition. by Robert J. Daigle, BA, RVT, FSVU Produced by Summer Publishing. LLC
This collection is designed to aid instructors and students that are using the textbook Techniques in Noninvasive Vascular Diagnosis. Summer Publishing authorizes and licenses the use of this COPYRIGHTED material contained in this collection to the school educational program. Use of the slides, graphics, case studies or movies for endeavors outside the activities of the school is prohibited without written permission from Summer Publishing.

## Slide 2: Chapter 15. Transcranial Doppler Techniques In Noninvasive Vascular Diagnosis - 4th edition

## Slide 3: TCD “Free-hand” Method
No Imaging
Single crystal-2 MHz Doppler, multi-gated Doppler
Can be performed bilaterally, simultaneously with proper gear.
Notes: Free- Hand method relies on sample volume depth, flow direction and velocity to identify cerebral vascular anatomy, There is no B-mode image. Transducer is usually 2 MHz, and has a small “footprint”, an advantage when acoustic windows are small.

## Slide 4
Transcranial Doppler Imaging
Used phased array
B-mode image
Color Doppler
Spectral Doppler
Unilateral method

## Slide 5: Applications of TCD & TCI
Serial monitoring of MCA and other intracranial vessels for vasospasm.
Evaluation of intracranial aneurysm and arterio-venous malformation.
Basilar artery occlusion.
Intracranial ICA stenosis.
Notes: 4

## Slide 6: Applications of TCD and TCI
Adjunct to extracranial exam
Monitoring vasospastic effects of sickle cell anemia
Confirmation of brain death
Notes: 5

## Slide 7: Exclusive Applications of TCD
Microemboli detection during carotid surgery, CABG, and carotid PTA/stenting
Cerebral autoregulation - vasoreactivity to CO2
Detection of Rt. to Lt. cardiac shunts
Monitoring of real-time blood flow to brain during surgical procedures
Notes: When TCD transducear are fitted into a Halo device, the probes can be left in position to monitor MCA blood flow. Some systems have two channel capability for monitoring bilaterally.

## Slide 8: Head Gear for TCD Bilateral Monitoring
TCD Transducer
Notes: Transducers are affixed to each side in the temporal area.
Transcranial surveillance for micro-emboli and CO2 reactivity typically is performed using bilateral TCD transducers that monitor both hemispheres simultaneously, and record long periods of spectral Doppler information. For emboli monitoring in carotid endarterectomy, one TCD transducer may be used, but it must be held in place with an attachment system similar to that used in bilateral monitoring. These attachment systems are not currently available for transcranial color imaging transducers. The 2 MHz transducers are inserted into the lateral probe holders and adjusted to receive signal from the MCAs.

## Slide 9: Intracranial ICA Anatomy
Notes: The ophthalmic artery, feeding the eye, is the first major branch of the internal carotid artery.
Petrous ICA:Courses through the petrous portion of the temporal bone and is inaccessible to ultrasound.
Cavernous ICA, also known as the carotid siphon, consists of:
Parasellar portion.
Genu portion (the bend).
Supraclinoid portion (distal segment).

## Slide 10
Circle of Willis
ACA
anterior communicating a
anterior cerebral a
middle cerebral a
posterior communicating a
vertebral a
basilar a
posterior cerebral a
ICA
P1
P2
A2
A1

## Slide 11: Middle Cerebral Arteries (MCA)
Course laterally towards the temporal bone with a number of branches.
Carry 75-80% of ICA flow.
Larger than the ACAs.
M1 segment- from the MCA origin to the first branch.
M2 segment, MCA distal to the first branch.

## Slide 12: Anterior Cerebral Arteries (ACA)
Course medially towards the midbrain (A1 segment).
Give rise to the anterior communicating artery (AcoA). This vessel courses between the two ACAs.
A2 segment then courses anteriorly to supply the anterior segments of the brain.

## Slide 13: Incomplete Circle in Patient with ICA Occlusion
Normal circle
Atresic segments
ICA
ICA
ICA
Notes: Patients with incomplete circles are more likely to experience stroke in the present of carotid artery stenosis or occlusion, as collateral pathways are significantly reduced.
Posterior and anterior communicating arteries provide collateral pathways within the circle of Willis. In the presence of an ICA occlusion, flow from the contralateral ACA can "cross-fill" via the anterior communicationg artery, and course retrograde in the ipsilateral ACA to supply the MCA and the lateral hemisphere.

## Slide 14: Cerebral Collateral Pathways
Notes: Other collateral pathways that may develop with ICA occlusion include retrograde flow in the supraorbital and supratrochlear arteries, branches of the ophthalmic artery. This pathway reconstitutes the supraclinoid segment of the ICA with blood flow being supplied by communicating ECA branches.

## Slide 15: Posterior Cerebral Arteries (PCA)
Perfuse posterior hemisphere
Wrap around the cerebral peduncle.
P1 segment courses from origin (basilar a.) to posterior communicating artery (PCoA)
P2 segment is distal to the PCoA

## Slide 16: TCD Windows -Transtemporal
Over the temporal bone and superior to the zygomatic arch (cheek bone)
65-70% loss of ultrasound energy due to bone structure and size of acoustic “window”.
No access in 10% of population due to thickness of bone segment
Notes: Vessels accessible from the transtemporal window.

## Slide 17: TCD Windows –Transtemporal Arteries Accessible
MCA
ACA
MCA/ACA bifurcation.
PCA
Terminus ICA
PCoA and ACoA maybe, if functioning as collateral pathways with lots of flow
1. posterior
2. middle
3. anterior
Notes: Vessels accessible from the transtemporal window.

## Slide 18: TCD Windows - Transorbital
ICA siphon
Ophthalmic artery
Must use very low Doppler output power for this window

## Slide 19: TCD Windows-Suboccipital – Foramen Magnum
Basilar artery
Vertebral arteries

## Slide 20: Circle of Willis Anomalies
50% of population have an intact and functioning circle (estimated)
Only 25 % have the classic configuration
Notes: Many patients have a total occlusion of an ICA and are asymptomatic, whereas many with the condition suffer stroke. It is likely that the availability of collateral pathways effects the outcome. In those with a disrupted circle, the ability to perfuse from the contralateral side is impaired.

## Slide 21: TCD Method- MCA
Patient supine, operator at head of bed
Apply gel to temporal region
Use a large sample volume, 5-10 mm
Set sample volume depth to 50 mm
Use a “flashlight” technique moving transducer to locate the MCA
MCA Flow should be towards the Doppler beam

## Slide 22: TCD Method
Optimize Doppler signal and record waveforms
Do not angle correct, leave the angle cursor set to zero (parallel with the Doppler line.
Measure peak mean velocity
Do not use Doppler invert

## Slide 23: TCD – Vessel Identification
Depth of vessel (by range gate)
Flow direction
Mean velocity value

## Slide 24: Mean Velocity for TCD
Notes: Report not flow direction and measure peak-mean velocity

## Slide 25: TCD Method- Bifurcation
Move the sample volume (SV) to a shallower MCA depth, then “step” the SV towards the MCA/ACA bifurcation
Record bidirectional flow at the bifurcation at 5.5 - 6.5 cm depth
Angle the transducer slightly anterior, increase SV depth and identify the ACA
ACA flow is away from the transducer

## Slide 26: TCD Method - ACA
ACA flow is away from the transducer
Follow the ACA depth to midline at 7.5- 8.0 cm
Record waveforms and measure mean velocity
ACA velocity should be less than the MCA

## Slide 27: TCD Method - PCA
Start with SV at bifurcation depth and angle transducer posteriorly and inferiorly.
Once a separate signal is detected move SV depth to 75 mm. Flow in the P1 segment should be “towards”.

## Slide 28: Depths and Flow Direction- Transtemporal

## Slide 29: Suboccipital Window

## Slide 30: Suboccipital – Foramen Magnum Vessels accessible:
basilar
vertebrals

## Slide 31: TCD Method –Vertebral Basilar
Patient lying on side, pillow under head with chin tucked in towards chest
Place transducer to one side of midline , and 1 inch below base of skull.
Start with SV depth at 60 mm, aim at bridge of nose to identify vertebral artery
Flow should be “Away”

## Slide 32: TCD Method –Vertebral Basilar
Record and measure waveforms
Follow the course of the VA, by stepping the SV, to the basilar artery (BA) (depth 80-90 mm).
Record basilar artery waves, flow should be away.
Flow should be “Away”
Follow BA as far (deep) as possible

## Slide 33: Depths and Flow Direction-Suboccipital

## Slide 34: Transorbital
Place the transducer over closed eyelid and aim in a slight posterior direction and slightly towards midline.
Set the SV to 50 mm for the OA.
NOTE: The system transmit power should be reduced to 15% for this approach to prevent damage to the eye.

## Slide 35: Transorbital
Flow should be towards the transducer.
Step the SV along the length of the OA to the ICA at approximately 55-70 mm depth.
OA flow is high resistance, ICA flow is low resistance

## Slide 36: Depths and Flow Direction-Transorbital

## Slide 37: Transcranial Color Doppler Imaging (TCI)
B-Mode imaging
Color Doppler
Pulsed Doppler
Way easier than TCD
Small footprint, low frequency phased array transducer, 1-3 or 4 MHz

## Slide 38: TCI Method
From trans temporal window, identify the temporal lobe of the brain, or the boney structures near the lobe.
Set field of view to 12-14 cm
The MCA will course along the anterior side of the temporal lobe.
Turn on color and optimize

## Slide 39: TCI Anatomy- Transtemporal

## Slide 40: TCI

## Slide 41: TCI Method
The onscreen orientation is the same for both the left and right sides
Follow the same methods as TCD
Verify flow direction and obtain mean velocity measurements in all vessels

## Slide 42: MCA
Flow is “towards”
Depth 3.0- 6.0 cm
Mean velocity 55 cm/s +/- 12 cm/s
Notes: TAP = “time average peak” or peak mean velocity.

## Slide 43: MCA / ACA Bifurcation
Flow is “bidirectional”
SV Depth 5.6-6.5 cm

## Slide 44: Anterior Cerebral Artery (ACA) (A1)
Flow is “away”
Depth 6.0-8.0 cm
Mean velocity 50 cm/s +/- 11 cm/s

## Slide 45: Posterior Cerebral Artery (PCA)

## Slide 46: Posterior Cerebral Artery (PCA)
Notes: Peduncle is also called mesencephalic brain stem, looks like rabbit’s feet.

## Slide 47: Posterior Cerebral Artery (PCA)
P1- flow towards
Depth 6-7 cm
P2- flow away
Mean vel. 39 cm/sec. +/- 10cm/sec.

## Slide 48: Vertebro-Basilar

## Slide 49: Cerebral Aneurysm
Aneurysm rupture – approx. 28,000 individuals annually
Mortality rate exceeds 50%
Survivors face aneurysm clipping
Subarachnoid hemorrhage (SAH) may cause cerebral vessel vasospasm; if severe, can result in stroke.

## Slide 50: Cerebral Aneurysm
Spasm is commonly delayed in onset
Serial TCD or TCI monitoring can detect the onset, severity, and effects of treatment
Treatment may include potent vasodilators and/or angioplasty

## Slide 51: Cerebral Vasospasm
Vasospasm:
range = mild >> severe
May occur in any major cerebral vessel
Basilar a spasm
vertebrals

## Slide 52: Cerebral Vasospasm Symptoms
Confusion
Decreased level of consciousness
“Goofiness”
Stroke
Death

## Slide 53: Vasospasm Method
If necessary, have the patient sedated
Move or remove temporal bandages
Use sterile acoustic gel on the side of the incision
Use transtemporal window, perform a bilateral baseline TCD/TCI exam
The most common vessel involved is the MCA

## Slide 54: Vasospasm Method
Investigate the entire MCA with color and spectral Doppler
Look for regions of focal velocity acceleration
Record the highest mean velocity, note the depth of SV for follow-up
Diagnosis of vasospasm is based on high mean velocity

## Slide 55: TCD - MCA Vasospasm
Normal 30 – 80 cm/sec
Mild 120 –140 cm/sec (hyperemia ?)
Moderate 140 – 200 cm/sec
Severe > 200 cm/sec
Some labs include an MCA / ICA ratio (mean velocities). ≥ 6.0 ratio is consistent with severe vasospasm
Mean velocities (cm / sec)
Notes: 2

## Slide 56: TCD Chart for Vasospasm
Notes: Typical chart for serial follow-up of patients post op for aneurysm or sub arachnoid hemorrhage. This is demonstrated in the next case.

## Slide 57: Patient S.G.
46 yr. old female incurred a SAH 6/26/--
Left MCA aneurysm clipped 6/26
Angio #1, 6/28, no significant spasm
7/10 progression to severe Rt. MCA spasm Angio confirmation and Papavarine administered into Rt. MCA
7/11, 480 mg Papavarine Rt. MCA
7/12, 250 mg Papavarine Rt. MCA
Notes: 5
A catheter was placed (from the groin) to the spasm location and Papavarine, a vasodilator medicine, was injected.

## Slide 58
Patient SG: SAH from Lt. MCA Aneurysm 6/26
severe
moderate
mild
MCA mean velocity
dates
P
P
P
10
A = angiogram P = Papavarine administration
A
Notes: Based on TCI data, 3 papavarine injections were performed on the R MCA on 7/10, 11, 12. TCI Exam on 7/13 indicated spasm was reduced with velocity in the moderate range.
There was a spike in the Lt. MCA velocity on 7/19. Patient was not treated as she was improving neurologically.

## Slide 59
RT MCA spasm, 7/10
LT MCA 7/10
Patient SG: severe spasm RT MCA
R MCA vel= 193
L MCA vel= 75

## Slide 60
Rt MCA severe spasm
Mean vel. = 227 cm/s
Lt MCA mean vel. 48 cm/s
Patient SG.

## Slide 61: SG Outcome
Patient was discharged 7/24
Returned for follow-up one month later and was without symptoms 

## Slide 62: TCD for MCA Vasospasm Problems
Skull penetration
Brain swelling (displaces anatomy depth)
Metals clips can block US signal
Patient cooperation
Notes: 10

## Slide 63: Cerebral Emboli Detection
The following can cause emboli to the cerebral vessels
  Cardiac surgery
  Carotid endarterectomy
  Carotid angioplasty & stenting
TCD can be used to detect emboli during the procedures
Notes: 8

## Slide 64: Cerebral Emboli
High Intensity Transient Signals (HITS) AKA, Micro-embolic Signals (MES)
Air- bubbles (have a chirping sound on Doppler)
Particulate matter (platelets, atheromatous debris)

## Slide 65: Emboli Detection: Intraoperative Monitoring
Performed with head gear and 2 TCD transducers for bilateral exam
Assess bilateral MCAs
Unilateral exams also possible

## Slide 66: Emboli Detection: intraoperative monitoring
TCI is not used for monitoring
Monitoring usually performed for at least 20 minutes
Automatic emboli counter software is useful to count # of MES
Problem: MES or artifact??

## Slide 67: Emboli Detection: intraoperative monitoring
High-end TCD systems use multiple sample gates for each Doppler
MES can be “plotted” as they course through multiple MCA sample volumes
Color M-mode is also used to detect emboli

## Slide 68: M-Mode with 4 spectral sample gates per side
Bilateral TCD System

## Slide 69
MCA with spectral
Doppler and audio
Spectrum.
Example of a MES

## Slide 70
Figure A: a microemboli
Figure B: an artifact, diffuse audio signal
Figure C: a “shower” of emboli

## Slide 71: Microembolic Signal
Duration less than 300 msec.
Signal is unidirectional within the Doppler spectrum (unless it’s a shower)
Snap or chirp sound on Doppler audio
Should appear in all unilateral Doppler SVs.

## Slide 72: Emboli and strokes in carotid endarterectomy and stents
TCD monitoring used during carotid PTA with stenting and CEA (carotid endarterectomy)
40 patients for PTA with stenting
75 patients for CEA
Jordan WD, et al. Microemboli detected by TCD monitoring in patients during carotid angioplasty versus carotid endarterectomy. Cardiovascular Surgery Jan 1999 Vol 7 No1

## Slide 73: Jordan
For stents, 74 emboli per stenosis with 4 neurologic events
For CEA. 9 emboli per stenosis, 1 neurologic event
CEA stroke patient had 48 MES

## Slide 74: Jordan- Conclusion
PTA with stenting 8x more microemboli than CEA
Higher neurologic complication rate is associated with high microembolic rate
Larger study needed to determine association of MES to higher morbidity-mortality.

## Slide 75: Detection of Rt. to Lt. Cardiac Shunts and PFO
PFO = Patent Foramen Ovale

## Slide 76: Ischemic Stroke
Represents the third greatest cause of death in the western word
Is the greatest cause of functional incapacity
Origin is undetermined in 40% of cases according to conventional etiological criteria
Sacco R.L.,et al, Infarcts of undetermined cause: the NINCDS Stroke Data Bank. Ann. Neurol. 1989:25:382-390

## Slide 77: Cryptogenic Stroke
Stroke of unknown etiology
Suspicion of paradoxical brain emboli arising from the venous circulation
Emboli from the venous system can pass to the arterial circulation through a righ to left cardiac shunt or PFO.

## Slide 78: Paradoxical Brain Emboli (PBE)
Emboli whose source is not from an identifiable source in the arterial system
Also referred to as venous-to-arterial emboli

## Slide 79: Patent Foramen Ovale (PFO)
A connection between the left and right atria
Due to inadequate postnatal closure of the Foramen Ovale.
Can allow emboli arising in the venous system to pass to the arterial circulation

## Slide 80: Prevalence of PFO
Young stroke patients 40-50%
Patients with cryptogenic stroke 42-77%
Normal controls 10-30%

## Slide 81: Patent Foramen Ovale

## Slide 82: Test for PFO
Patient supine, Intravenous line is placed,
Bilateral TCD headgear is mounted and MCA Doppler signals obtained
Micro bubbles created by mixing saline and air is injected into the IV line
Patient then performs a valsalva maneuver.
If no Rt. to Lt. shunt, bubbles go to lungs and dissipate

## Slide 83: Test for PFO
If shunt exists, bubbles will go to the MCA and are detected with bilateral TCD monitoring.
A micro bubble “shower” occurs

## Slide 84
Normal TCD bubble test
with bilateral MCA monitoring
R
L
2 sample gates per side, one at 52 mm depth, the other at 56 mm

## Slide 85: Positive TCD Bubble Test